## Slide 1
FORBES SAFETY SOLUTIONS
ASBESTOS & LEAD AWARENESS
Identification, Health Risks & Protective Measures
Ref: 29 CFR 1926.1101 (Asbestos) | 29 CFR 1926.62 (Lead)
TOOLBOX TALK

## Slide 2
KEY STATISTICS
~3,000 Cases/Year
Mesothelioma diagnoses in the U.S. — nearly all from asbestos exposure
~500,000 Children
Have blood lead levels above the CDC reference value in the U.S.
Pre-1980 Buildings
Highest risk for asbestos-containing materials and lead-based paint
Source: CDC/ATSDR, EPA Lead Information

## Slide 3
WHERE ARE THESE MATERIALS FOUND?
Asbestos: floor tiles, ceiling tiles, pipe insulation, pipe wrap, roofing materials, joint compound
Asbestos: boiler insulation, duct wrap, spray-applied fireproofing, transite panels
Lead: paint in pre-1978 buildings (most common source), solder in plumbing joints
Lead: glazed ceramics, imported consumer products, some industrial coatings
If you suspect ACM (asbestos-containing material) or LBP (lead-based paint) — STOP WORK immediately
Do NOT disturb, cut, sand, or demolish suspected materials — report to your supervisor at once
Testing and survey by qualified professionals is required before any demolition or renovation work
Source: 29 CFR 1926.1101 | 29 CFR 1926.62

## Slide 4
HEALTH EFFECTS
Asbestos exposure causes mesothelioma, lung cancer, and asbestosis — often with 10-40 year latency
There is no safe level of asbestos exposure — even brief disturbances can release deadly fibers
Asbestos fibers are microscopic and cannot be seen, smelled, or tasted
Lead poisoning affects the nervous system, kidneys, reproductive system, and brain development
Acute lead exposure: abdominal pain, fatigue, headaches, muscle/joint pain
Chronic lead exposure: memory loss, mood disorders, reduced cognitive function, organ damage
Workers can carry lead dust home on clothing — endangering family members (take-home exposure)
Source: CDC/ATSDR | OSHA Health Effects Guidance

## Slide 5
CONTROLS & PPE REQUIREMENTS
Never use power tools, dry sweeping, or compressed air on suspected ACM or LBP — creates airborne hazards
Wet methods: keep materials damp to minimize fiber/dust release during any authorized disturbance
HEPA vacuums required for cleanup — standard shop vacuums spread fine particles into the air
PPE for asbestos: minimum half-face respirator with P100 filters, disposable coveralls, gloves
PPE for lead: respirator appropriate to exposure level, coveralls, gloves, shoe covers
Decontamination: use designated wash stations; do not eat, drink, or smoke in work areas
Only trained and licensed abatement workers may perform removal of ACM or LBP
Source: 29 CFR 1926.1101 | 29 CFR 1926.62

## Slide 6
QUIZ — TEST YOUR KNOWLEDGE
Q1: What should you do if you suspect you've found asbestos-containing material?
A: Stop work immediately, do not disturb the material, and report it to your supervisor.
Q2: Why are HEPA vacuums required instead of regular shop vacuums?
A: Standard vacuums cannot capture fine asbestos fibers or lead dust and spread them into the air.
Q3: Name two common locations where lead-based paint is found on construction sites.
A: Pre-1978 building surfaces (walls, trim, doors) and plumbing solder joints.

## Slide 7
SIGN-OFF SHEET
Asbestos & Lead Awareness
# | Print Name | Signature | Company | Date
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
Forbes Safety Solutions