## Slide 1
FORBES SAFETY SOLUTIONS
Back Safety &
Proper Lifting
[Company Name]
[Date]
Ref: OSHA General Duty Clause, NIOSH Lifting Equation

## Slide 2
FORBES SAFETY SOLUTIONS
Why This Matters
1 in 5
Workplace injuries
are back-related
$100B+
Annual cost of
back injuries
in the U.S.
51 lbs
NIOSH recommended
weight limit under
ideal conditions

## Slide 3
Proper Lifting Technique
1. Plan the Lift
Assess the weight, check your path, and decide if you need help or mechanical aids before lifting.
2. Get Close
Stand as close to the load as possible. The farther the load is from your body, the greater the strain on your back.
3. Bend at the Knees
Squat down by bending your knees — not your waist. Keep your back straight and chest forward.
4. Get a Firm Grip
Use your full hand, not just your fingers. Ensure the load is stable before lifting.
5. Lift with Your Legs
Straighten your legs to lift. Let your leg muscles do the work, keeping the load close to your body.
6. No Twisting
Turn with your feet, not your torso. Twisting while carrying a load is a leading cause of back injuries.

## Slide 4
Additional Back Safety Measures
Team Lifts
If a load exceeds 51 lbs or is awkward to handle, get a partner. Communicate clearly — one person leads the lift.
Mechanical Aids
Use dollies, hand trucks, forklifts, or hoists whenever available. Mechanical aids dramatically reduce injury risk.
Stretching & Warm-Up
Begin each shift with light stretching. Cold muscles are more prone to strains and tears.
Body Positioning
Avoid reaching overhead or bending at the waist for extended periods. Reposition materials to waist height when possible.
Know Your Limits
If a load feels too heavy, it probably is. Never risk injury to save time — ask for help.

## Slide 5
NIOSH Lifting Equation — Key Factors
The NIOSH Recommended Weight Limit (RWL) starts at 51 lbs and is reduced by multipliers based on the conditions below. If conditions are not ideal, the safe lifting weight drops significantly.
Factor | Description | Impact
Horizontal Distance | How far the load is from your body | Farther = lower safe weight
Vertical Location | Height of the load at start of lift | Very high/low = reduced limit
Vertical Travel | How far you move the load up/down | Greater distance = more strain
Asymmetry Angle | Degree of twisting during the lift | Twisting reduces safe weight
Frequency | How often you lift per minute | More frequent = lower limit
Coupling Quality | Quality of handles or grip | Poor grip = reduced safe weight

## Slide 6
Quiz / Discussion
Q1: What body part should do the heavy lifting — your back or your legs?
A: Your legs. Keep your back straight and use your leg muscles to power the lift.
Q2: What is the NIOSH recommended weight limit under ideal conditions?
A: 51 pounds. This limit decreases when conditions are not ideal.
Q3: What should you do if a load feels too heavy?
A: Stop and ask for help. Use a team lift or mechanical aid — never risk injury.

## Slide 7
ATTENDANCE SIGN-OFF
# | Name (Print) | Signature | Date
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  |