## Slide 1
FORBES SAFETY SOLUTIONS
CAUGHT-IN /
CAUGHT-BETWEEN
HAZARDS
OSHA Focus Four — 29 CFR 1926
TOOLBOX TALK
[Company Name]
[Date]

## Slide 2
WHY THIS MATTERS
Caught-In/Between: The Last of OSHA's "Focus Four" Hazards
5–7%
of Construction
Fatalities
Caught-in/between is
one of the "Fatal Four"
18–24
Deaths Per Year
Workers killed annually
in caught-in/between incidents
#4
Focus Four
Hazard
Joins falls, struck-by,
and electrocution
Source: OSHA Fatal Four Statistics / Bureau of Labor Statistics Census of Fatal Occupational Injuries

## Slide 3
TYPES OF CAUGHT-IN/BETWEEN HAZARDS
MACHINERY
Caught in unguarded rotating parts (gears, rollers, augers)
Clothing, hair, or jewelry pulled into running equipment
Hand/fingers caught in moving belt or chain drive
EQUIPMENT & OBJECTS
Crushed between backing equipment and a fixed object
Caught between equipment swing radius and a wall or post
Pinch points between moving and stationary machine parts
COLLAPSING MATERIALS
Trench cave-in burying workers
Collapsing stacked materials or unsecured loads
Structural collapse during demolition or excavation
Reference: 29 CFR 1926 Subpart P (Excavations) | 29 CFR 1910.212 (Machine Guarding)

## Slide 4
PREVENTION MEASURES
CATEGORY | PREVENTION MEASURES
Machine Guarding & LOTO | • All moving parts must have guards in place (29 CFR 1910.212) • Lockout/Tagout before ANY maintenance or adjustment • Never reach into operating machinery
Personal Precautions | • No loose clothing, jewelry, or long hair near rotating equipment • Never position body between equipment and immovable objects • Stay clear of equipment swing radius at all times
Trench & Excavation Safety | • Trench protective systems required at 5 ft depth • Sloping, shoring, or shielding per competent person • Never enter an unprotected trench — no exceptions
Equipment & Vehicles | • Use spotters when backing heavy equipment • Establish barricades around swing radius areas • Never walk between operating equipment and structures

## Slide 5
REAL-WORLD SCENARIOS
SCENARIO | HAZARD TYPE | WHAT WENT WRONG | PREVENTION
Clothing caught in unguarded auger | Caught In — Machinery | Machine guard removed, loose sleeve pulled worker in | Replace guard; no loose clothing policy; LOTO for cleaning
Worker crushed between backing truck and wall | Caught Between — Equipment | No spotter; worker in blind spot between truck and structure | Use spotter; establish exclusion zone; high-vis vest
Trench cave-in buries worker | Caught In — Collapse | No protective system; trench deeper than 5 ft without shoring | Trench box or sloping; competent person inspection
Hand caught in conveyor belt | Caught In — Machinery | Worker cleared jam without shutting down conveyor | LOTO before clearing jam; never reach into running equipment
Discuss: Has anyone on this crew witnessed or experienced a caught-in/between near miss?

## Slide 6
QUIZ / DISCUSSION
1
Name the three types of caught-in/between hazards.
Answer: Caught in running machinery, caught between equipment and fixed objects, and caught in collapsing materials (e.g., trench cave-in).
2
At what depth must trench protective systems be used?
Answer: 5 feet. Trenches 5 feet or deeper require protective systems (sloping, shoring, or shielding) unless excavated in stable rock.
3
What must be done before performing maintenance on equipment with moving parts?
Answer: Lockout/Tagout (LOTO) — De-energize the equipment and apply lock and tag to prevent unexpected startup.

## Slide 7
TOOLBOX TALK SIGN-OFF
Caught-In / Caught-Between Hazards
# | PRINT NAME | SIGNATURE | COMPANY | DATE
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
FORBES SAFETY SOLUTIONS | Presenter: ________________ | Location: ________________