## Slide 1
FORBES SAFETY SOLUTIONS
Working in Cold Weather
Ref: OSHA Cold Stress Guidance | NIOSH Cold Stress Publication
[Company Name]
[Date]
TOOLBOX TALK

## Slide 2
WHY THIS MATTERS
~700
Workers die annually in the U.S. from environmental heat and cold exposure combined
-25°F
Wind chill at which exposed skin can develop frostbite in as little as 15 minutes
95°F
Below this core body temperature, hypothermia begins — confusion, shivering, and loss of coordination set in

## Slide 3
Cold-Related Illnesses: Recognize the Signs
HYPOTHERMIA
Core body temp drops below 95°F
Early signs: shivering, fatigue, confusion, loss of coordination
Severe: slurred speech, drowsiness, slow pulse, loss of consciousness
First Aid: Move to warm area, remove wet clothing, warm center of body first, give warm beverages (no alcohol), seek EMS immediately
FROSTBITE & TRENCH FOOT
Frostbite: skin freezes — numbness, waxy appearance, white/gray patches on ears, nose, fingers, toes
Do NOT rub affected area — warm gently with body heat or warm (not hot) water
Trench foot: prolonged exposure to cold, wet conditions — swelling, numbness, blisters
Prevention: keep feet dry, change wet socks frequently, air out boots at breaks

## Slide 4
Cold Weather Protection Strategies
LAYERING SYSTEM
Base layer: moisture-wicking (polyester, merino wool) — never cotton
Mid layer: insulating (fleece, down) — traps body heat
Outer layer: wind/waterproof shell — blocks wind chill and rain/snow
Protect extremities: insulated gloves, warm hat (40% heat loss from head), face covering in extreme cold
WORK PRACTICES
Schedule warm-up breaks every 60-90 minutes in heated areas
Use buddy system — watch coworkers for signs of cold stress
Chemical hand/toe warmers in gloves and boots
Stay hydrated — dehydration increases cold injury risk even in winter
Monitor wind chill factor — not just temperature

## Slide 5
Wind Chill Risk Levels
Wind Chill Temp | Risk Level | Action Required
Above 20°F | Low risk | Standard cold weather PPE, regular monitoring
20°F to 0°F | Moderate risk | Warm breaks every 60 min, buddy system required
0°F to -20°F | High risk | Warm breaks every 40 min, limit exposure time
-20°F to -40°F | Very high risk | 15-min max exposure, heated enclosures required
Below -40°F | Extreme danger | Non-emergency outdoor work should be suspended
— | All levels | Ensure warm beverages available, emergency warming shelter on site

## Slide 6
QUIZ / DISCUSSION
1
What are the three layers of a proper cold-weather layering system?
Answer: Base layer (moisture-wicking), mid layer (insulating fleece/down), and outer layer (wind/waterproof shell).
2
What should you NOT do if a coworker shows signs of frostbite?
Answer: Do not rub or massage the frostbitten area — this can cause further tissue damage. Warm gently with body heat or warm water.
3
Why is hydration still important when working in cold weather?
Answer: Dehydration increases the risk of cold-related injuries. Cold air is dry and your body still loses moisture through breathing and sweating under heavy layers.

## Slide 7
ATTENDANCE SIGN-OFF
Working in Cold Weather
# | Print Name | Signature | Company | Date
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
By signing above, I confirm that I attended this toolbox talk and understand the material presented.