## Slide 1
FORBES SAFETY SOLUTIONS
Eye & Face
Protection
[Company Name]
[Date]
Ref: 29 CFR 1926.102, ANSI Z87.1

## Slide 2
FORBES SAFETY SOLUTIONS
Why This Matters
2,000
Workplace eye
injuries per day
requiring treatment
90%
Of eye injuries are
preventable with
proper eyewear
$300M+
Annual cost of
workplace eye
injuries in the U.S.

## Slide 3
Common Eye & Face Hazards
Flying Debris
Cutting, chipping, grinding, and drilling generate high-speed particles that can penetrate the eye
Grinding Sparks
Metal grinding produces hot sparks and fragments that cause severe burns and corneal damage
Chemical Splash
Solvents, acids, caustics, and cleaning agents can cause permanent eye damage on contact
UV Radiation
Welding arcs, sunlight, and cutting torches emit UV that causes painful flash burns (arc eye)
Dust & Fine Particles
Concrete dust, sawdust, and insulation fibers cause irritation, scratches, and infections

## Slide 4
Types of Eye & Face Protection
Safety Glasses
Impact-rated lenses with side shields. Required for general construction work. Must meet ANSI Z87.1 — look for the "Z87+" marking on the lens.
Safety Goggles
Sealed fit around the eyes. Required for chemical splash, dust exposure, and high-impact tasks where debris can enter from sides.
Face Shields
Full-face coverage. Used over safety glasses for grinding, chipping, and chemical handling. Not standalone protection.
Welding Helmets
Auto-darkening or fixed-shade lenses for welding and cutting operations. Proper shade number based on the welding process.

## Slide 5
Best Practices & ANSI Z87.1 Markings
Best Practices
Wear eye protection at all times on site
Inspect lenses for scratches and damage daily
Use anti-fog coatings in humid environments
Ensure side shields are always attached
Prescription safety glasses must also meet Z87.1
Replace damaged or scratched eyewear immediately
Clean lenses with approved lens cleaner only
ANSI Z87.1 Markings
Marking | Meaning
Z87+ | High-impact rated
Z87 | Basic impact rated
D3 | Splash/droplet protection
D4 | Dust protection
D5 | Fine dust protection
W (shade #) | Welding shade filter
U (scale #) | UV filter rating

## Slide 6
Quiz / Discussion
Q1: What percentage of eye injuries are preventable with proper PPE?
A: 90% — the vast majority of eye injuries can be avoided with correct eyewear.
Q2: What marking on safety glasses indicates high-impact rating?
A: Z87+ stamped on the lens confirms it meets ANSI high-impact standards.
Q3: Can a face shield be worn alone as eye protection?
A: No — face shields must always be worn over safety glasses or goggles.

## Slide 7
ATTENDANCE SIGN-OFF
# | Name (Print) | Signature | Date
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  |