## Slide 1
FORBES SAFETY SOLUTIONS
PORTABLE GENERATOR SAFETY
Carbon Monoxide, Electrical Hazards & Safe Operation
Ref: 29 CFR 1926.405 | OSHA/NIOSH Generator Safety Guidance
TOOLBOX TALK

## Slide 2
KEY STATISTICS
~70 Deaths/Year
From carbon monoxide poisoning linked to portable generators
900+ ER Visits/Year
CO poisoning incidents involving portable generators
#1 Generator Hazard
Carbon monoxide — odorless, colorless, and deadly
Source: U.S. Consumer Product Safety Commission (CPSC)

## Slide 3
CARBON MONOXIDE & PLACEMENT
NEVER operate a generator indoors, in garages, basements, or any enclosed/partially enclosed space
Place generators at least 20 feet from buildings with exhaust directed away from doors, windows, and vents
CO is odorless and colorless — you cannot detect it without a monitor
Early CO poisoning symptoms: headache, dizziness, nausea, confusion, weakness
Advanced symptoms: loss of consciousness, brain damage, death — can occur in minutes
Use battery-operated CO detectors in nearby occupied spaces when generators are running
If anyone shows CO symptoms, move to fresh air immediately and call 911
Source: OSHA/NIOSH Generator Safety Guidance

## Slide 4
ELECTRICAL HAZARDS & GFCI PROTECTION
Always use a Ground Fault Circuit Interrupter (GFCI) when connecting tools or equipment
Properly ground the generator per manufacturer instructions and 29 CFR 1926.405
Never plug a generator directly into a building's wiring (backfeeding) — use a transfer switch
Inspect power cords for damage before each use — replace frayed or cut cords immediately
Keep generators dry; do not operate in rain or wet conditions without proper cover
Never overload a generator — know the wattage rating and total connected load
Use heavy-duty, outdoor-rated extension cords with adequate wire gauge
Source: 29 CFR 1926.405 | OSHA Electrical Safety Standards

## Slide 5
FUEL HANDLING & STORAGE
Turn off the generator and let it cool completely before refueling — fuel on a hot engine can ignite
Store fuel in approved containers away from the generator and any ignition sources
Never store fuel indoors or near occupied buildings
Keep a fire extinguisher rated for flammable liquids (Class B) near the generator at all times
Do not smoke near generators or fuel storage areas
Inspect fuel lines and connections for leaks before starting
Follow manufacturer lockout/tagout procedures for maintenance and repairs
Source: OSHA/NIOSH Generator Safety Guidance

## Slide 6
QUIZ — TEST YOUR KNOWLEDGE
Q1: How far from buildings should a portable generator be placed?
A: At least 20 feet away, with exhaust directed away from doors, windows, and vents.
Q2: Why must you use a GFCI with a portable generator?
A: To protect against electrical shock from ground faults in connected equipment.
Q3: Why should you never refuel a generator while it is running?
A: Fuel spilled on a hot engine can ignite and cause a fire or explosion.

## Slide 7
SIGN-OFF SHEET
Portable Generator Safety
# | Print Name | Signature | Company | Date
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
Forbes Safety Solutions