## Slide 1
GHS / HAZARD COMMUNICATION
& SDS READING
Understanding Chemical Labels, Pictograms, and Safety Data Sheets
Reference: 29 CFR 1910.1200 | Globally Harmonized System (GHS)
FORBES SAFETY SOLUTIONS

## Slide 2
KEY STATISTICS
50,000+
Hazardous chemicals used in U.S. workplaces
32M
Workers potentially exposed to chemical hazards annually
16
Standardized sections in every Safety Data Sheet

## Slide 3
GHS PICTOGRAMS — THE 9 HAZARD SYMBOLS
Flame — flammable gases, liquids, solids, aerosols, and self-reactive substances
Flame Over Circle — oxidizers that can cause or intensify fire
Exploding Bomb — explosives, self-reactive chemicals, and organic peroxides
Skull and Crossbones — acutely toxic substances — fatal or toxic if swallowed, inhaled, or through skin contact
Corrosion — causes severe skin burns, eye damage, or corrodes metals
Health Hazard (person) — carcinogens, mutagens, reproductive toxins, respiratory sensitizers, organ toxicity
Exclamation Mark — irritants, narcotic effects, skin sensitizers, acute toxicity (less severe)
Gas Cylinder — compressed, liquefied, dissolved, or refrigerated gases under pressure
Environment — aquatic toxicity — hazardous to the aquatic environment (not mandatory under OSHA)

## Slide 4
SDS 16-SECTION FORMAT — KEY SECTIONS
Section 1 — Identification — product name, manufacturer, emergency phone number
Section 2 — Hazard(s) Identification — GHS classification, signal word, pictograms, hazard & precautionary statements
Section 4 — First-Aid Measures — symptoms, required treatment by route of exposure (inhalation, skin, eye, ingestion)
Section 8 — Exposure Controls / PPE — permissible exposure limits (PELs), engineering controls, required PPE
Sections 9–11 — Physical/chemical properties, stability/reactivity, and toxicological information
Sections 14–16 — Transport, regulatory, and other information including revision date

## Slide 5
EMPLOYEE RIGHTS AND CONTAINER LABELING
Right to Know — every employee has the legal right to access SDS for any chemical in their workplace
SDS Location — SDS binders or digital access must be available at all times during the shift — know where yours are
Container Labels Must Include — product name, signal word (Danger or Warning), GHS pictograms, hazard statements, and precautionary statements
Secondary Containers — must be labeled with product name and hazards when transferred from the original container
Never Remove Labels — defaced or missing labels must be replaced immediately — an unlabeled container is a violation
Training Requirement — employers must train workers on HazCom at hire and whenever a new chemical hazard is introduced

## Slide 6
KNOWLEDGE CHECK
Which SDS section tells you what PPE is required when working with a chemical?
A) Section 2 — Hazard Identification
B) Section 4 — First-Aid Measures
C) Section 8 — Exposure Controls / PPE
D) Section 11 — Toxicological Information
Answer: C) Section 8 — Exposure Controls / Personal Protective Equipment.

## Slide 7
GHS / HAZCOM & SDS READING — SIGN-OFF
All attendees must print and sign below to confirm understanding of this topic.
# | PRINT NAME | SIGNATURE | DATE
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  | 
FORBES SAFETY SOLUTIONS