## Slide 1
FORBES SAFETY SOLUTIONS
HAND & POWER
TOOL SAFETY
29 CFR 1926.300-307 | 29 CFR 1910.242-244
TOOLBOX TALK
[Company Name]
[Date]

## Slide 2
WHY THIS MATTERS
Tools Are Involved in Hundreds of Thousands of Injuries Every Year
110K
Hand Tool ER
Visits / Year
Workers sent to the
emergency room annually
400K
Power Tool ER
Visits / Year
Injuries from power tools
requiring medical treatment
510K+
Total Annual
Tool Injuries
Combined hand and power
tool injuries each year
Source: Bureau of Labor Statistics / U.S. Consumer Product Safety Commission

## Slide 3
HAND TOOL SAFETY
CATEGORY | KEY PRACTICES
Inspection & Condition | • Inspect all tools before each use • Remove damaged tools from service immediately • No mushroomed heads on chisels or wedges
Proper Use | • Use the right tool for the job — no improvising • Proper wrench sizing — never use cheater bars • Keep cutting tools sharp (dull = more force = less control)
Carrying & Storage | • Carry tools in a belt or bucket, not pockets • Never carry tools loose in hands while climbing • Store tools properly — designated racks and boxes
Housekeeping | • Return tools to proper storage after use • Keep work area clear of unused tools • Secure tools at height to prevent dropped objects

## Slide 4
POWER TOOL SAFETY
CATEGORY | KEY PRACTICES
Guards & Safety Devices | • All guards must be in place before operation • Never remove or bypass safety guards • Trigger locks — use and verify function
Electrical Safety | • Use grounded or double-insulated tools only • Inspect cords for damage before each use • GFCI protection required on construction sites
Powder-Actuated Tools | • Only certified/trained operators may use • Treat like a loaded firearm — never point at anyone • Test fire into approved material before each shift
General Rules | • Disconnect power before changing accessories • Keep cords clear of cutting path and heat • Never carry a tool by its cord

## Slide 5
PPE REQUIREMENTS FOR TOOL USE
TASK / TOOL | EYE | FACE SHIELD | HEARING | GLOVES
Grinding / Cutting | Required | Required | Required | Task-specific
Drilling / Hammering | Required | Recommended | As needed | Task-specific
Powder-Actuated Tools | Required | Required | Required | Required
Hand Tools | Required | As needed | As needed | Task-specific
Saws (circular, recip.) | Required | Recommended | Required | Anti-vibration
Always match gloves to the task — cut-resistant for sharp materials, anti-vibration for power tools, leather for hot work.

## Slide 6
QUIZ / DISCUSSION
1
What should you do before using any tool on the jobsite?
Answer: Inspect it. Check for damage, defects, or wear. Remove damaged tools from service immediately — never use a defective tool.
2
Why is using a dull cutting tool more dangerous than a sharp one?
Answer: A dull tool requires more force to cut, reducing control and increasing the chance of the tool slipping and causing injury.
3
Who is permitted to operate a powder-actuated tool?
Answer: Only workers who have been trained and certified on that specific tool. Treat it like a firearm — never point at anyone.

## Slide 7
TOOLBOX TALK SIGN-OFF
Hand & Power Tool Safety
# | PRINT NAME | SIGNATURE | COMPANY | DATE
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
FORBES SAFETY SOLUTIONS | Presenter: ________________ | Location: ________________