## Slide 1
FORBES SAFETY SOLUTIONS
Housekeeping on
Construction Sites
[Company Name]
[Date]
Ref: 29 CFR 1926.25 — Housekeeping

## Slide 2
FORBES SAFETY SOLUTIONS
Why This Matters
25%
Of all workplace
injuries involve
slips, trips & falls
#1
OSHA violation
cited on
construction sites
3x
Higher fire risk
with poor
housekeeping

## Slide 3
Key Hazards from Poor Housekeeping
Slips, Trips & Falls
Debris, spills, uneven surfaces, and cluttered walkways cause the most common construction injuries
Fire Hazards
Accumulated waste materials, oily rags, and blocked fire exits dramatically increase fire risk
Puncture Wounds
Protruding nails are the #1 cause of puncture wounds on job sites — boards must be de-nailed or stacked safely
Delayed Emergency Response
Blocked aisles and cluttered exits prevent quick evacuation and slow emergency responder access
Pest & Health Issues
Improperly stored food waste and standing water attract pests and create unsanitary conditions

## Slide 4
Housekeeping Best Practices
Clear Walkways
Maintain unobstructed paths at all times. Remove debris, cords, and materials from travel routes immediately.
Material Storage
Stack materials neatly and securely. Keep stored items away from edges, walkways, and overhead power lines.
Scrap & Waste Removal
Remove waste materials regularly throughout the day. Don't let debris accumulate — use designated waste areas.
Nail Management
Bend or remove protruding nails from lumber immediately. Never leave boards with nails facing upward.
Tool Organization
Return tools to designated areas after use. Never leave tools on scaffolds, ladders, or elevated surfaces.
Dumpster Management
Keep dumpster areas clear. Don't overfill containers. Schedule regular pickup to prevent overflow.

## Slide 5
End-of-Shift Cleanup Checklist
All walkways and stairways clear of debris
Tools returned to storage or gang boxes
Scrap materials removed to designated waste area
Protruding nails bent or removed from lumber
Electrical cords coiled and stored properly
Flammable materials stored in approved containers
Dumpsters and waste bins not overfilled
Work area swept and materials stacked securely

## Slide 6
Quiz / Discussion
Q1: What is the #1 cause of puncture wounds on construction sites?
A: Protruding nails in lumber and scrap boards.
Q2: Name three hazards that result from poor housekeeping.
A: Slips/trips/falls, fire hazards, puncture wounds, delayed emergency response, pest issues.
Q3: When should cleanup occur — only at end of shift?
A: No — housekeeping should be ongoing throughout the day, with a thorough cleanup at end of shift.

## Slide 7
ATTENDANCE SIGN-OFF
# | Name (Print) | Signature | Date
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  |