## Slide 1
FORBES SAFETY SOLUTIONS
LADDER
SAFETY
Toolbox Talk | 29 CFR 1926.1053
[Company Name]
[Date]

## Slide 2
WHY THIS MATTERS
22,710
Ladder injuries treated
in emergency rooms
annually (BLS)
161
Fatal falls from ladders
per year in the U.S.
(BLS Census of Fatal Injuries)
#1
Falls are the leading
cause of death in
construction (OSHA)
Falls are an OSHA "Focus Four" Hazard
Ladder-related incidents account for a significant share of fall injuries and fatalities on construction sites. Most ladder accidents are preventable — caused by improper setup, wrong ladder selection, overreaching, or failure to inspect before use. Following OSHA standards and basic safe practices saves lives.
Source: OSHA Fall Prevention, BLS Census of Fatal Occupational Injuries

## Slide 3
LADDER TYPES, RATINGS & SETUP RULES
Ladder Types & Duty Ratings
Type | Rating | Capacity
Type IAA — Special Duty | Extra Heavy | 375 lbs
Type IA — Industrial | Extra Heavy | 300 lbs
Type I — Industrial | Heavy Duty | 250 lbs
Type II — Commercial | Medium Duty | 225 lbs
Type III — Household | Light Duty | 200 lbs
Construction requires Type I, IA, or IAA
Setup Rules (Extension Ladders)
4-to-1 ratio: For every 4 ft of height, set the base 1 ft out from the wall
Extend 3 feet above the landing or upper support point
Secure the top of the ladder to prevent displacement — tie off or have a spotter
Set on a firm, level surface — never on boxes, barrels, or unstable ground
Lock all spreaders and extension locks before climbing
Face the ladder when ascending or descending — always
Source: 29 CFR 1926.1053

## Slide 4
THREE-POINT CONTACT & PRE-USE INSPECTION
Three-Point Contact Rule
Always maintain three points of contact when climbing or descending:
— Two hands + one foot, or
— Two feet + one hand
Do NOT carry tools or materials in your hands while climbing — use a tool belt, hoist line, or bucket
Never overreach — keep your belt buckle between the side rails
Move one hand or foot at a time
Grip the rungs, not the side rails (better grip if foot slips)
Pre-Use Inspection Checklist
Inspect BEFORE EVERY USE — remove defective ladders from service immediately
Check rungs/steps for cracks, bends, corrosion, or missing components
Verify locking mechanisms (spreaders, extension locks) engage fully
Look for grease, oil, mud, or wet/slippery surfaces on rungs and feet
Check safety feet / pads — must be intact and non-slip
Ensure all labels (duty rating, safety instructions) are legible
Metal ladders: check for dents, bends, or damage to rails
Fiberglass ladders: check for chips, cracks, or UV degradation
Source: OSHA Ladder Safety QuickCard

## Slide 5
COMMON VIOLATIONS & WHEN NOT TO USE A LADDER
Common OSHA Violations
Using a damaged or defective ladder
Not extending 3 ft above the landing point
Setting up at wrong angle (too steep or too shallow)
Standing on the top cap or top rung of a stepladder
Using a metal ladder near electrical hazards
Overloading — exceeding the duty rating (body weight + tools + materials)
Placing on uneven or unstable surfaces
Using a ladder horizontally as a scaffold plank
When NOT to Use a Ladder
Use scaffolding or an aerial lift instead when:
Work requires both hands for an extended period
Task duration exceeds 15-30 minutes at height
Heavy materials or tools must be brought up
Work height exceeds ladder capacity or safe reach
Multiple workers need simultaneous elevated access
High wind conditions or adverse weather
Work is near power lines (use fiberglass + maintain clearance, or use a non-conductive lift)
Source: 29 CFR 1926.1053, OSHA Fall Protection Standards

## Slide 6
QUIZ / DISCUSSION QUESTIONS
1. What is the correct setup angle for an extension ladder?
Answer: 4-to-1 ratio — for every 4 feet of height, the base is 1 foot away from the wall
2. What does "three-point contact" mean, and why is it important?
Answer: Always maintain two hands and one foot, or two feet and one hand on the ladder. It prevents falls caused by loss of balance.
3. Name two situations where you should use scaffolding or an aerial lift instead of a ladder.
Answer: When work requires both hands for extended periods, when task duration exceeds 15-30 min, when heavy materials must be transported, or when multiple workers need access.

## Slide 7
ATTENDANCE & SIGN-OFF
Ladder Safety | [Date] | [Company Name]
# | Printed Name | Signature | Date
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  | 
FORBES SAFETY SOLUTIONS