## Slide 1
FORBES SAFETY SOLUTIONS
NIGHT WORK & LOW-VISIBILITY SAFETY
Illumination, High-Visibility Clothing & Fatigue Management
Ref: 29 CFR 1926.56 (Illumination) | ANSI/ISEA 107
TOOLBOX TALK

## Slide 2
KEY STATISTICS
2x Higher Fatality Rate
Night-shift construction workers face roughly double the fatal injury risk
Class 2 Minimum
High-visibility garments required for all construction workers near traffic
5 Foot-Candles
Minimum illumination required for general construction areas per OSHA
Source: OSHA, ANSI/ISEA 107, BLS Fatality Data

## Slide 3
LIGHTING REQUIREMENTS
OSHA 29 CFR 1926.56 sets minimum foot-candle requirements by work area:
General construction areas and concrete placement: 5 foot-candles minimum
General construction plants and shops: 10 foot-candles minimum
Indoor warehouses, corridors, hallways, and exit ways: 5 foot-candles minimum
First aid stations, offices, and shops: 30 foot-candles minimum
Position temporary lighting to eliminate dark spots, shadows, and glare
Secure all temporary lighting fixtures to prevent them from falling or being knocked over
Source: 29 CFR 1926.56 — OSHA Illumination Standards

## Slide 4
HIGH-VISIBILITY CLOTHING & EQUIPMENT
ANSI/ISEA 107 Class 2 garments minimum for all workers in low-visibility conditions
Class 3 garments required for flaggers working at night (full body visibility)
Hi-vis garments must include retroreflective striping — not just fluorescent color
Replace garments when retroreflective material is faded, torn, or dirty enough to reduce visibility
Equip all mobile equipment with retroreflective markings and functional lighting
Use cones, delineators, and barricades with reflective sheeting to mark hazard zones
Ensure backup alarms and strobe lights are operational on all equipment used at night
Source: ANSI/ISEA 107 | MUTCD Standards

## Slide 5
FATIGUE, COMMUNICATION & AWARENESS
Night shift workers have elevated fatigue risk — schedule regular breaks and rotate tasks
Recognize fatigue warning signs: difficulty concentrating, slow reactions, irritability, microsleeps
Communication is harder at night — use radios, hand signals with illuminated wands, and spotters
Brief crews on changed site conditions before each night shift begins
Wildlife awareness: nocturnal animals (snakes, rodents, insects) are more active — watch your step
Maintain clear access to emergency routes and ensure they are well-lit at all times
Report any lighting failures, dark areas, or visibility concerns immediately to your supervisor
Source: OSHA Night Work Guidance | NIOSH Fatigue Management

## Slide 6
QUIZ — TEST YOUR KNOWLEDGE
Q1: What is the minimum foot-candle requirement for general construction areas?
A: 5 foot-candles, as required by OSHA 29 CFR 1926.56.
Q2: What class of high-visibility garment must flaggers wear during night work?
A: Class 3 garments, which provide full-body visibility with retroreflective striping.
Q3: Name two strategies for managing fatigue during night shifts.
A: Schedule regular breaks and rotate tasks to keep workers alert and reduce error risk.

## Slide 7
SIGN-OFF SHEET
Night Work & Low-Visibility Safety
# | Print Name | Signature | Company | Date
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
Forbes Safety Solutions