## Slide 1
Pinch Points &
Crushing Hazards
Recognizing and Avoiding Compression Injuries on the Job
Ref: 29 CFR 1910.212, 29 CFR 1926.300
Forbes Safety Solutions

## Slide 2
The Danger of Pinch Points
125K+
Hand and finger injuries occur in U.S. workplaces each year — many from pinch points
#2
Hand injuries rank as the second most common workplace injury type across all industries
80%
Of pinch point injuries are preventable with proper guarding and awareness

## Slide 3
Where Pinch Points Occur
Between two moving parts: gears, rollers, belt drives, and chain sprockets
Between a moving part and a stationary object: press rams, closing doors, swing-radius of excavators
Rotating equipment: drill presses, lathes, augers, and power take-offs (PTOs)
During material handling: setting steel, lowering loads, stacking pipe, closing gates and tailgates
Between the ground and moving equipment: tracks, outriggers, and lowering platforms
Always ask: 'Where could my hands, fingers, or body get caught between two objects?'
Ref: 29 CFR 1910.212, 29 CFR 1926.300

## Slide 4
Machine Guarding & Hand Placement
Never remove or bypass machine guards — they are engineered barriers between you and moving parts
If a guard is missing or damaged, stop work and report it immediately — do not operate the equipment
Keep your hands and fingers away from pinch points — use push sticks, pliers, or other tools to feed material
Be aware of hand placement when guiding loads, closing doors, or connecting components
Use lockout/tagout (LOTO) procedures before reaching into any area with moving parts for maintenance or clearing jams
Barricade pinch point areas where workers could inadvertently enter the danger zone
Ref: 29 CFR 1910.212, 29 CFR 1926.300

## Slide 5
Glove Selection & Body Positioning
Wear cut-resistant or impact gloves when handling materials with pinch hazards — they provide critical protection
NEVER wear gloves near rotating equipment (drills, lathes, grinders) — gloves can catch and pull your hand in
Know the difference: gloves protect from pinch/crush between objects, but create entanglement hazards with rotating parts
Position your body to avoid the line of fire — never place any body part where it could be caught if equipment shifts
Maintain situational awareness: watch for swing radius of equipment, moving conveyors, and closing mechanisms
Communicate with coworkers before moving loads or operating equipment to ensure everyone is clear of pinch points
Ref: 29 CFR 1910.212, 29 CFR 1926.300

## Slide 6
Knowledge Check
Q1: Name two locations where pinch points commonly occur on a job site.
A: Between two moving parts (gears, rollers) and between a moving part and stationary object (press rams, closing doors).
Q2: When should you NOT wear gloves around equipment?
A: Near rotating equipment such as drills, lathes, and grinders — gloves can catch and pull your hand into the machine.
Q3: What should you do if a machine guard is missing or damaged?
A: Stop work immediately, do not operate the equipment, and report the missing guard to supervision.

## Slide 7
Pinch Points & Crushing Hazards — Sign-Off Sheet
By signing below, I confirm I attended this Toolbox Talk and understand the material presented.
# | Print Name | Signature | Date
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  |