## Slide 1
RESPIRATORY PROTECTION AWARENESS
Selecting, Fitting, and Using Respirators on the Jobsite
Reference: 29 CFR 1910.134
FORBES SAFETY SOLUTIONS

## Slide 2
KEY STATISTICS
5M+
U.S. workers required to wear respirators on the job
#4
29 CFR 1910.134 is the 4th most cited OSHA standard
90%
Of respiratory injuries are preventable with proper protection

## Slide 3
WHEN RESPIRATORS ARE NEEDED AND TYPES AVAILABLE
When Required — whenever engineering controls alone cannot reduce airborne contaminants below the PEL or when IDLH conditions exist
Filtering Facepiece (N95) — disposable half-mask that filters particles; does not protect against gases or vapors
Half-Face Respirator — reusable mask covering nose and mouth; accepts cartridges for particulates, gases, or combination
Full-Face Respirator — covers entire face including eyes; provides higher protection factor and splash protection
PAPR — Powered Air-Purifying Respirator — uses a blower to pull air through filters; ideal for extended wear
SCBA — Self-Contained Breathing Apparatus — supplies clean air from a tank; required for IDLH and unknown atmospheres

## Slide 4
FIT TESTING, SEAL CHECKS, AND FACIAL HAIR
Fit Testing Requirement — every tight-fitting respirator user must pass an initial fit test and annual retest per 29 CFR 1910.134(f)
Qualitative vs. Quantitative — qualitative uses taste/smell agents; quantitative uses instruments to measure leakage — both are OSHA-accepted
User Seal Check — Every Time — positive and negative pressure seal checks must be performed each time the respirator is donned
Facial Hair Prohibition — beards, stubble, or sideburns that interfere with the seal are prohibited for tight-fitting respirators
Medical Evaluation — a physician or licensed healthcare professional must clear a worker medically before respirator use
Documentation — fit test results, medical clearances, and training records must be maintained by the employer

## Slide 5
CARTRIDGE SCHEDULES, IDLH, AND MAINTENANCE
Cartridge Change Schedules — employer must establish a change schedule based on contaminant type, concentration, humidity, and breathing rate
End-of-Service Indicators — some cartridges have ESLI; if not, a written change schedule is mandatory — never rely on smell alone
IDLH Situations — Immediately Dangerous to Life or Health — requires SCBA or airline respirator with escape bottle
Buddy System — at least one standby person must be present outside the IDLH area with rescue equipment
Inspection and Storage — inspect before and after each use; store in a clean, sealed container away from contaminants and sunlight
Never Alter Equipment — do not modify respirators, remove valves, or use unapproved parts — doing so voids NIOSH certification

## Slide 6
KNOWLEDGE CHECK
How often must a user perform a seal check on a tight-fitting respirator?
A) Once per shift
B) Only during the annual fit test
C) Every time the respirator is put on
D) Weekly
Answer: C) Every time — a positive and negative pressure seal check is required each time the respirator is donned.

## Slide 7
RESPIRATORY PROTECTION AWARENESS — SIGN-OFF
All attendees must print and sign below to confirm understanding of this topic.
# | PRINT NAME | SIGNATURE | DATE
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  | 
FORBES SAFETY SOLUTIONS