## Slide 1
FORBES SAFETY SOLUTIONS
SILICA DUST
EXPOSURE
Toolbox Talk | 29 CFR 1926.1153
[Company Name]
[Date]

## Slide 2
WHY THIS MATTERS
2M+
Construction workers
exposed to silica dust
in the U.S. annually
100%
Silicosis is irreversible
and has no cure —
prevention is critical
#1
Leading cause of
occupational lung
disease in construction
What is Respirable Crystalline Silica?
Silica is a mineral found in concrete, brick, block, mortar, stone, and sand. When these materials are cut, ground, drilled, or crushed, tiny dust particles become airborne and can be inhaled deep into the lungs — causing silicosis, lung cancer, COPD, and kidney disease.
Source: OSHA Silica Standard, CDC/NIOSH

## Slide 3
OSHA PEL & COMMON EXPOSURE SOURCES
OSHA Permissible Exposure Limit (PEL): 50 μg/m³ (8-hour TWA)
Where Silica Is Found
Concrete and cement products
Brick, block, and mortar
Natural stone and granite
Sand and gravel
Engineered stone countertops
Asphalt (contains sand/aggregate)
High-Risk Tasks
Cutting concrete or masonry with a saw
Grinding or polishing concrete surfaces
Drilling into rock, concrete, or block
Demolition of concrete structures
Mixing dry concrete or mortar
Sweeping or blowing concrete dust
Source: 29 CFR 1926.1153

## Slide 4
REQUIRED CONTROLS (TABLE 1 COMPLIANCE)
Task / Equipment | Engineering Control | Respiratory Protection
Handheld power saw | Integrated water delivery to suppress dust | None when controls used per Table 1
Walk-behind saw | Integrated water delivery to suppress dust | None when controls used per Table 1
Jackhammer / Breaker | Continuous water feed at point of impact | APF 10 respirator when controls used
Grinder (4.5" or smaller) | Vacuum with HEPA filter attached to guard | APF 10 respirator when controls used
Drill (handheld) | Vacuum with HEPA filter or water delivery | None when controls used per Table 1
Indoor sweeping / cleanup | Wet sweeping or HEPA-filtered vacuum | APF 10 respirator
Source: OSHA Table 1 — Specified Exposure Control Methods

## Slide 5
RESPIRATORY PROTECTION & MEDICAL SURVEILLANCE
Respiratory Protection
Required when engineering controls alone don't reduce exposure below the PEL (50 μg/m³)
Minimum: NIOSH-approved N95 filtering facepiece (APF 10)
Higher exposures may require half-face or full-face respirators with P100 filters
Workers must be fit-tested annually and medically cleared before use
Employers must have a written Respiratory Protection Program per 29 CFR 1910.134
Medical Surveillance
Required for workers exposed above the Action Level (25 μg/m³) for 30+ days/year
Baseline exam within 30 days of initial assignment
Follow-up exams every 3 years (minimum)
Includes: medical history, chest X-ray, pulmonary function test (spirometry)
Employer must cover all costs and provide results to the worker in writing
Workers diagnosed with silicosis must be referred to a specialist
Source: 29 CFR 1926.1153, 29 CFR 1910.134

## Slide 6
QUIZ / DISCUSSION QUESTIONS
1. What is OSHA's Permissible Exposure Limit (PEL) for respirable crystalline silica in construction?
Answer: 50 μg/m³ as an 8-hour time-weighted average (TWA)
2. Name two engineering controls that can be used to reduce silica dust exposure when cutting concrete.
Answer: Integrated water delivery (wet cutting) and vacuum dust collection systems with HEPA filtration
3. How often must medical surveillance exams be conducted for workers exposed above the Action Level?
Answer: Baseline exam within 30 days of initial assignment, then every 3 years at minimum

## Slide 7
ATTENDANCE & SIGN-OFF
Silica Dust Exposure | [Date] | [Company Name]
# | Printed Name | Signature | Date
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  | 
FORBES SAFETY SOLUTIONS