## Slide 1
FORBES SAFETY SOLUTIONS
SLIPS, TRIPS, AND FALLS
Leading Causes, Prevention & Good Housekeeping
Ref: 29 CFR 1926.25 (Housekeeping) | 29 CFR 1926 Subpart M
TOOLBOX TALK

## Slide 2
KEY STATISTICS
#1 Cause of Death
Falls are the leading cause of fatalities in the construction industry
~25% of All Injuries
Slips, trips, and falls account for roughly one-quarter of all workplace injuries
OSHA Focus Four
Falls are one of OSHA's Focus Four hazards — the top causes of construction deaths
Source: BLS Census of Fatal Occupational Injuries | OSHA

## Slide 3
COMMON CAUSES OF SLIPS, TRIPS & FALLS
Wet, oily, or greasy surfaces — spills not cleaned up promptly
Uneven ground, potholes, or changes in floor level without markings or ramps
Cluttered walkways with tools, materials, or debris blocking the path
Poor lighting in work areas, stairways, corridors, and access points
Cords, hoses, welding leads, or air lines running across walkways without covers
Missing or damaged handrails on stairs, ramps, and elevated platforms
Weather conditions: ice, mud, rain, and wet leaves create slippery surfaces
Improper footwear lacking slip-resistant soles or adequate ankle support
Source: OSHA | 29 CFR 1926.25

## Slide 4
PREVENTION STRATEGIES
Housekeeping: clean as you go — keep walkways clear of tools, scrap, and debris at all times
Clean up spills immediately; use absorbent material and post wet floor warnings
Wear proper footwear with slip-resistant, sturdy soles appropriate for the work environment
Use three-point contact (two hands and one foot, or two feet and one hand) on ladders and stairs
Slow down on wet, icy, or uneven surfaces — take smaller steps to maintain balance
Cover or ramp all cords, hoses, and lines crossing walkways; use cord covers or elevate them
Ensure adequate lighting in all work areas — request temporary lighting where needed
Report hazards immediately: broken stair treads, missing covers, damaged guardrails, spills
Source: 29 CFR 1926.25 | 29 CFR 1926 Subpart M

## Slide 5
FALL PROTECTION & GUARDRAILS
Fall protection required at 6 feet in construction (29 CFR 1926 Subpart M)
Guardrail systems: top rail at 42" (+/- 3"), midrail at 21", toeboards at floor level
Inspect guardrails daily — never remove or bypass them without implementing alternate protection
Floor holes and wall openings must be covered or guarded; mark covers 'HOLE' or 'COVER'
Personal fall arrest systems: full-body harness, shock-absorbing lanyard, and secure anchor point
Inspect all fall protection equipment before each use — remove damaged items from service
Training: every worker must understand the fall hazards of their specific tasks and the controls in place
Source: 29 CFR 1926 Subpart M | OSHA Fall Protection Standards

## Slide 6
QUIZ — TEST YOUR KNOWLEDGE
Q1: At what height is fall protection required in the construction industry?
A: 6 feet above a lower level, per 29 CFR 1926 Subpart M.
Q2: What does 'three-point contact' mean when climbing a ladder?
A: Always maintain two hands and one foot, or two feet and one hand, in contact with the ladder.
Q3: Name three common causes of slips, trips, and falls on construction sites.
A: Wet surfaces, cluttered walkways, and cords/hoses running across paths without covers.

## Slide 7
SIGN-OFF SHEET
Slips, Trips, and Falls
# | Print Name | Signature | Company | Date
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
Forbes Safety Solutions