## Slide 1
Spotter & Backing Safety
Preventing Struck-By Incidents During Vehicle & Equipment Operations
Ref: 29 CFR 1926.601-602
Forbes Safety Solutions

## Slide 2
Backing Accident Statistics
~70
Workers struck by backing vehicles on construction sites each year
Top 10
Backing accidents rank among the leading causes of construction fatalities nationwide
90%
Of backing incidents are preventable with proper spotter use and safe backing procedures

## Slide 3
Spotter & Driver Responsibilities
A spotter's sole duty is to guide the driver — never perform other tasks while spotting
The spotter must maintain constant visual contact with the driver and remain visible at all times
Position yourself where the driver can see you in mirrors or directly — never stand in the vehicle's path of travel
Use standardized hand signals: stop (closed fist raised), back up (arm extended with beckoning motion), turn left/right (arm pointing direction)
The driver must stop immediately if they lose sight of the spotter — no exceptions
Establish a communication plan before starting: agree on signals, path, and hazards
Ref: 29 CFR 1926.601-602

## Slide 4
When Spotters Are Required & Blind Spots
A spotter is required whenever the driver's view is obstructed, near pedestrians, in congested areas, or near excavations and drop-offs
Common blind spots: directly behind the vehicle, right side of dump trucks, rear of loaders and excavators, all sides of large cranes
Walk around the vehicle before backing — check for workers, tools, materials, and uneven ground (the 360-degree walk-around)
Backup cameras and alarms are aids — they are NOT replacements for a trained spotter
Never assume a path is clear because it was clear moments ago — conditions on active job sites change constantly
Ref: 29 CFR 1926.601-602

## Slide 5
Best Practices for Backing Safety
Minimize backing whenever possible — plan routes that allow forward-only travel or pull-through parking
Use a spotter for every backing operation near workers, structures, or limited-visibility areas
Sound the horn before backing — even when a spotter is present — to alert nearby workers
Back slowly and smoothly — maintain a speed that allows instant stopping
Ensure all workers in the area are aware of vehicle movements and maintain safe distances
Report any near-misses immediately — these are opportunities to prevent future incidents
Ref: 29 CFR 1926.601-602

## Slide 6
Knowledge Check
Q1: What should a driver do if they lose sight of their spotter?
A: Stop the vehicle immediately and do not move until visual contact with the spotter is re-established.
Q2: Are backup cameras and alarms an acceptable substitute for a spotter?
A: No. Cameras and alarms are aids only — they do not replace a trained spotter.
Q3: What is the 360-degree walk-around, and when should it be done?
A: A complete visual inspection around the vehicle before backing to check for workers, obstacles, and hazards.

## Slide 7
Spotter & Backing Safety — Sign-Off Sheet
By signing below, I confirm I attended this Toolbox Talk and understand the material presented.
# | Print Name | Signature | Date
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  |