## Slide 1
FORBES SAFETY SOLUTIONS
STRUCK-BY HAZARDS
OSHA Focus Four — Toolbox Talk
[Company Name]
[Date]
Reference: 29 CFR 1926 Subpart M | OSHA Focus Four

## Slide 2
WHY THIS MATTERS
Struck-by incidents are one of OSHA's "Focus Four" — the leading causes of death in construction.
~75
Fatal struck-by
injuries per year
in construction
~15%
Of all construction
fatalities are
struck-by incidents
#2
Leading cause of
death on construction
sites (BLS data)
Source: BLS Census of Fatal Occupational Injuries, OSHA Focus Four

## Slide 3
FOUR TYPES OF STRUCK-BY HAZARDS
FLYING OBJECTS
Objects propelled through the air by a tool, machine, or explosive force. Examples: debris from grinding/cutting, nail gun projectiles, pneumatic tool fragments.
FALLING OBJECTS
Objects that fall from an upper level. Examples: tools dropped from scaffolding, unsecured materials on elevated surfaces, bricks or concrete from demolition.
SWINGING OBJECTS
Objects that swing and strike a worker. Examples: crane loads turning or swinging unexpectedly, a beam or panel rotating during rigging, equipment booms swinging.
ROLLING OBJECTS
Objects that roll and strike a worker. Examples: pipes or cylinders on slopes, vehicles/equipment rolling or backing over workers, unsecured wheel-mounted equipment.

## Slide 4
COMMON STRUCK-BY SCENARIOS
SCENARIO | HAZARD | KEY CONTROL
Unsecured materials falling from elevated work | Falling object | Toe boards, screens, debris nets, hard hats below
Equipment backing over workers on site | Rolling object | Spotters, backup alarms, exclusion zones, high-vis vests
Flying debris from cutting, grinding, or chipping | Flying object | Face shields, safety glasses, machine guards, barriers
Swinging crane loads striking workers | Swinging object | Tag lines, never stand under loads, signal person
Tools or materials dropped from scaffolds | Falling object | Tool tethering, toe boards, barricaded areas below

## Slide 5
PREVENTION MEASURES
PERSONAL PROTECTIVE EQUIPMENT
Hard hats — required in all active work areas
Face shields and safety glasses for cutting/grinding
High-visibility vests near mobile equipment
Steel-toe boots in all construction areas
Metatarsal guards when heavy objects are handled
ENGINEERING & WORK PRACTICES
Toe boards and screens on scaffolds
Secure all loads — never leave materials unsecured at height
Tag lines on all suspended loads
Equipment backup alarms and spotters
Never stand under suspended loads
Tool tethering when working at height
Barricade and sign hazardous areas below overhead work

## Slide 6
QUIZ / DISCUSSION
Q1
Name the four types of struck-by hazards.
Answer: Flying objects, falling objects, swinging objects, and rolling objects.
Q2
What should you always use when working near crane operations to control a suspended load?
Answer: Tag lines — and never stand directly under a suspended load.
Q3
A coworker is grinding steel without a face shield. What should you do?
Answer: Stop the task, remind them of the PPE requirement, and ensure they put on a face shield and safety glasses before resuming.

## Slide 7
ATTENDANCE SIGN-OFF
By signing below, I acknowledge that I attended and understood this Toolbox Talk on Struck-By Hazards.
# | PRINTED NAME | SIGNATURE | DATE
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  |