## Slide 1
Working Near Water —
Drowning Prevention
Protecting Workers from Drowning Hazards on Construction Sites
Ref: 29 CFR 1926.106
Forbes Safety Solutions

## Slide 2
Drowning Risks in Construction
~30
Construction workers die from drowning each year in the United States
6 ft
PFDs are required when working within 6 feet of water where a drowning hazard exists
< 60s
Cold water shock can incapacitate even strong swimmers in under 60 seconds

## Slide 3
When PFDs & Rescue Equipment Are Required
Personal flotation devices (PFDs) are required for all workers within 6 feet of water where a drowning hazard exists
PFDs must be U.S. Coast Guard-approved and properly fitted — test the fit before each use
Ring buoys with at least 90 feet of line must be available at 200-foot intervals along waterfront operations
Rescue skiffs or boats must be immediately available where workers are over water on barges or platforms
Swimming ability is NOT a substitute for wearing a PFD — even strong swimmers drown in workplace incidents
Flotation devices must be provided on all barges, over-water platforms, and temporary structures above water
Ref: 29 CFR 1926.106

## Slide 4
Cold Water, Flash Floods & Environmental Hazards
Cold water shock: sudden immersion in cold water triggers involuntary gasping and rapid breathing — you can inhale water in seconds
Cold water also causes rapid loss of muscle control — swimming ability drops dramatically within 3-5 minutes
Be alert to flash flood hazards when working in or near storm drains, culverts, channels, and low-lying areas
Monitor weather conditions — stop work and evacuate if flooding is forecast or water levels begin to rise
Never enter flooded areas to retrieve equipment or materials — the risk is not worth it
Be aware of currents even in seemingly calm water — moving water exerts enormous force on the body
Ref: 29 CFR 1926.106

## Slide 5
Rescue Procedures & Best Practices
Know the site rescue plan before starting work — identify rescue equipment locations, trained rescuers, and emergency contacts
Practice 'reach, throw, row, go': first reach with a pole, throw a ring buoy, use a boat — entering the water is the last resort
Only trained personnel should attempt in-water rescues — an untrained rescuer often becomes a second victim
Ensure all workers near water are trained in basic water rescue and CPR/first aid
Inspect PFDs and rescue equipment daily — replace damaged or expired gear immediately
Post warning signs near all water hazards and brief every worker during site orientation
Ref: 29 CFR 1926.106

## Slide 6
Knowledge Check
Q1: At what distance from water must workers wear PFDs?
A: Within 6 feet of water where a drowning hazard exists.
Q2: Why is swimming ability NOT an acceptable substitute for a PFD?
A: Even strong swimmers can be incapacitated by cold water shock, currents, or fatigue — PFDs keep you afloat regardless.
Q3: What is the correct rescue sequence for a worker who has fallen into water?
A: Reach, throw, row, then go — entering the water is the last resort and only by trained rescuers.

## Slide 7
Working Near Water — Drowning Prevention — Sign-Off Sheet
By signing below, I confirm I attended this Toolbox Talk and understand the material presented.
# | Print Name | Signature | Date
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  |