## Slide 1
CONFINED SPACE ENTRY
29 CFR 1910.146 & 1926 Subpart AA
Presenter: ____________________ Date: ____________________
FORBES SAFETY SOLUTIONS
TOOLBOX TALK

## Slide 2
WHY THIS MATTERS
From 2011 to 2018, 1,030 workers died in confined spaces — an average of 129 deaths per year (BLS Census of Fatal Occupational Injuries).
More than 60% of confined space fatalities are would-be rescuers. The worker who goes in to save a buddy without proper equipment becomes the second victim.
Atmospheric hazards are invisible killers: hydrogen sulfide (H2S) deadens your sense of smell at high concentrations, carbon monoxide (CO) is odorless, and oxygen-deficient air gives no warning before you collapse.
Permit-required confined spaces account for the majority of fatalities. The permit exists to force you through a checklist that keeps you alive.
Construction now has its own confined space standard (29 CFR 1926 Subpart AA) — if you're in construction, you must follow it, not just the general industry rule.
Source: BLS Confined Space Fatalities Fact Sheet
FORBES SAFETY SOLUTIONS

## Slide 3
ATMOSPHERIC TESTING & PERMIT ELEMENTS
Test the atmosphere BEFORE entry, in this order: (1) Oxygen — must be 19.5% to 23.5%, (2) Flammability (LEL) — must be below 10% of the lower explosive limit, (3) Toxics — H2S below 10 ppm, CO below 25 ppm.
Test at multiple levels — top, middle, and bottom of the space. Gases stratify: H2S is heavier than air (sinks), methane is lighter (rises), CO mixes evenly.
Continuous atmospheric monitoring during the entire entry, not just at the start. Conditions change — welding, coating, or disturbing sludge can release deadly gases instantly.
Entry permit must include: space identification, purpose of entry, date/time, authorized entrants, attendant name, atmospheric readings, rescue procedures, communication method, and entry supervisor signature.
Permit-required vs. non-permit: A permit-required space has a recognized hazard (atmospheric, engulfment, configuration, or other). You can reclassify to non-permit ONLY by eliminating all hazards and documenting the basis.
Source: OSHA 29 CFR 1910.146
FORBES SAFETY SOLUTIONS

## Slide 4
ATTENDANT DUTIES & RESCUE PLANNING
The attendant stays OUTSIDE the space for the entire entry. No exceptions. Their job is to monitor entrants, maintain communication, track who is inside, and summon rescue if anything goes wrong.
The attendant must NEVER enter the space to attempt rescue. This is how 60% of confined space deaths happen. Your job is to call for help, not become the next victim.
Communication must be continuous. If you lose contact with an entrant for any reason, initiate emergency procedures immediately — do not wait to see if they respond.
Rescue planning: Non-entry rescue (retrieval systems with tripods and winches) is preferred. Entry rescue requires a trained rescue team with SCBA on standby. "Call 911" is not a rescue plan — municipal responders may not arrive equipped for confined space rescue.
Every entrant must wear a chest or full-body harness attached to a retrieval line unless the retrieval line creates a greater hazard. The retrieval system must be in place and functional before anyone enters.
Source: CDC/NIOSH Confined Space Alert
FORBES SAFETY SOLUTIONS

## Slide 5
DISCUSSION QUESTIONS
Take 5 minutes to discuss with your crew:
1. Can you identify every confined space on this site? Which ones are permit-required and which are not?
2. If our gas monitor alarmed right now, what's the immediate procedure? Who do you contact first?
3. Who is the trained attendant for today's entry, and what are the three things they must never do?
4. If you saw a co-worker collapse in a confined space, what would you do — and what would you NOT do?
FORBES SAFETY SOLUTIONS

## Slide 6
ATTENDANCE SIGN-OFF
Date: ____________ Topic: Confined Space Entry Presenter: ____________________
# | PRINT NAME | COMPANY | SIGNATURE
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  | 
FORBES SAFETY SOLUTIONS