## Slide 1
PERMIT-REQUIRED CONFINED SPACE AWARENESS
Understanding Entry Hazards and Required Controls
Reference: 29 CFR 1910.146 | 29 CFR 1926 Subpart AA
FORBES SAFETY SOLUTIONS

## Slide 2
KEY STATISTICS
~100
Workers die in confined spaces in the U.S. every year
60%
Of confined space fatalities are would-be rescuers
#1
Atmospheric hazards are the leading cause of confined space deaths

## Slide 3
WHAT MAKES A SPACE "CONFINED" AND "PERMIT-REQUIRED"
Confined Space — Three Criteria — large enough to enter and perform work; has limited or restricted entry/exit; not designed for continuous occupancy
Permit-Required — Hazard #1 — contains or has the potential to contain a hazardous atmosphere (toxic, flammable, oxygen-deficient/enriched)
Permit-Required — Hazard #2 — contains material that could engulf or trap an entrant (grain, sand, water, sewage)
Permit-Required — Hazard #3 — has an internal configuration that could trap or asphyxiate (inwardly converging walls, sloping floors)
Permit-Required — Hazard #4 — contains any other recognized serious safety or health hazard (mechanical, electrical, thermal)
Key Rule — never enter any confined space without first determining if it is permit-required — assume it is until proven otherwise

## Slide 4
ATMOSPHERIC HAZARDS AND MONITORING
Oxygen Deficiency — below 19.5% O₂ is immediately dangerous; normal atmosphere is 20.9%
Oxygen Enrichment — above 23.5% O₂ creates extreme fire and explosion risk
Flammable Gases — monitor for LEL (Lower Explosive Limit); entry prohibited above 10% LEL
Toxic Gases — H₂S, CO, and other toxics must be below their PEL before entry
Continuous Monitoring — atmospheric testing must occur before entry and continuously throughout the work
Calibrated Instruments — all gas monitors must be bump-tested daily and calibrated per manufacturer requirements

## Slide 5
ROLES, PERMITS, AND RESCUE PLANS
Entrant — the worker who enters; must know the hazards, monitor conditions, and exit immediately if danger arises
Attendant — remains outside at all times; tracks entrants, monitors conditions, summons rescue — never enters
Entry Supervisor — authorizes entry by signing the permit; verifies all precautions are in place before work begins
The Permit — documents hazards, controls, atmospheric readings, rescue plan, and duration — posted at the entry point
Rescue Plan — non-entry retrieval (tripod + harness) is preferred; entry rescue only by trained rescue teams
Never Enter Without a Permit — even to retrieve a tool — an unauthorized entry can be fatal in seconds

## Slide 6
KNOWLEDGE CHECK
Which of the following is NOT one of the three criteria that define a confined space?
A) Large enough to enter and perform work
B) Contains a hazardous atmosphere
C) Has limited or restricted entry/exit
D) Not designed for continuous occupancy
Answer: B) A hazardous atmosphere makes it permit-required, but it is not one of the three defining criteria of a confined space.

## Slide 7
CONFINED SPACE AWARENESS — SIGN-OFF
All attendees must print and sign below to confirm understanding of this topic.
# | PRINT NAME | SIGNATURE | DATE
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  | 
FORBES SAFETY SOLUTIONS