## Slide 1
CRANE SIGNAL PERSON TRAINING
Standard Hand Signals and Communication Requirements
Reference: 29 CFR 1926.1419–1422
FORBES SAFETY SOLUTIONS

## Slide 2
KEY STATISTICS
250+
Crane-related deaths in the U.S. over the past decade
80%
Of crane accidents involve human error or miscommunication
100%
Of multi-crane lifts require a designated signal person

## Slide 3
SIGNAL PERSON QUALIFICATIONS & RESPONSIBILITIES
Qualified Signal Person — must be evaluated by a qualified third party or employer per OSHA 1926.1419
Know Standard Signals — must demonstrate proficiency in all standard hand signals before directing crane operations
Clear Line of Sight — signal person must maintain visual contact with operator at all times or use alternative communication
Competent in Load Path — must understand load dynamics, swing radius, and rigging to anticipate movements
Authority to Stop — any signal person can issue STOP and the operator must obey immediately
When Required — signals are mandatory when the operator cannot see the load, landing zone, or the path of travel

## Slide 4
STANDARD HAND SIGNALS — OSHA / ASME B30.5
Hoist — forearm vertical, index finger pointing up, move hand in small circles
Lower — arm extended downward, index finger pointing down, move hand in small circles
Swing — arm extended, point with finger in direction of swing of boom
Boom Up — arm extended, fingers closed, thumb pointing upward
Boom Down — arm extended, fingers closed, thumb pointing downward
Stop — arm extended, palm down, move arm back and forth horizontally
Emergency Stop — both arms extended, palms down, move arms back and forth horizontally
Dog Everything — clasp hands in front of body — halt all operations

## Slide 5
VOICE & RADIO SIGNALS AND LINE OF SIGHT
Voice / Radio Signals — permitted when hand signals are not practical due to distance, obstructions, or darkness
Dedicated Channel — radio communication must use a dedicated channel free from unrelated traffic
Confirm Before Moving — operator must repeat the signal back and receive confirmation before executing the movement
Line of Sight Required — if the signal person loses sight of the load or operator, all operations must stop immediately
Multiple Signal Persons — only one designated signal person directs at a time; transfer of duties must be clearly communicated
Signal Person Positioning — must stand in a safe location visible to the operator and clear of the swing radius and load path

## Slide 6
KNOWLEDGE CHECK
What hand signal requires BOTH arms extended, palms down, moving back and forth?
A) Stop
B) Dog Everything
C) Emergency Stop
D) Boom Down
Answer: C) Emergency Stop — both arms distinguish it from a regular stop (one arm).

## Slide 7
CRANE SIGNAL PERSON TRAINING — SIGN-OFF
All attendees must print and sign below to confirm understanding of this topic.
# | PRINT NAME | SIGNATURE | DATE
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  | 
FORBES SAFETY SOLUTIONS