## Slide 1
FORBES SAFETY SOLUTIONS
Rigging Safety Fundamentals
Ref: 29 CFR 1926.251 — Rigging Equipment for Material Handling
[Company Name]
[Date]
TOOLBOX TALK

## Slide 2
WHY THIS MATTERS
50+
Workers killed annually in crane and rigging-related incidents in construction
#1
Cause of rigging fatalities: being struck by a falling load due to rigging failure
60°
At a 60° sling angle, capacity is only 87% of rated — angle always affects capacity

## Slide 3
Sling Types & Selection
SLING TYPES
Wire Rope: high strength, good for heavy loads, heat-resistant, but inspect for broken wires and kinks
Synthetic Web: lightweight, won't mar loads, wide bearing surface — avoid near heat, chemicals, sharp edges
Alloy Steel Chain: excellent for high-heat and abrasive environments, durable — heavy to handle
Synthetic Round Slings: flexible, lightweight, protect load finish — vulnerable to cuts and UV damage
HITCH CONFIGURATIONS
Vertical Hitch: single leg, straight pull — 100% of rated capacity
Choker Hitch: sling wraps around load and through itself — 75% of rated capacity
Basket Hitch: sling cradles the load with both ends on hook — up to 200% of rated capacity (with balanced load at 90°)
Always verify hitch type matches the load shape, center of gravity, and weight

## Slide 4
Sling Angle Capacity Chart
Sling Angle | Capacity Factor | Example: 10,000 lb Rated Sling
90° (vertical) | 100% | 10,000 lbs
60° | 87% | 8,700 lbs
45° | 71% | 7,100 lbs
30° | 50% | 5,000 lbs
Below 30° | DO NOT USE | Sling stress exceeds safe limits
— | Rule | Never use slings at angles below 30° from horizontal

## Slide 5
Inspection, Signals & Safe Practices
SLING INSPECTION — REMOVE FROM SERVICE
Wire rope: 6+ broken wires in one lay, kinking, crushing, bird-caging, corrosion, heat damage
Synthetic web: cuts, tears, snags, acid/chemical burns, melting, excessive wear, missing labels
Chain: stretched or bent links, cracks, gouges, excessive wear (10%+ reduction)
All slings: missing or unreadable capacity tags, prior unauthorized modifications
SAFE RIGGING PRACTICES
Know the load weight — never guess; check shipping docs, calculate, or use a scale
Use tag lines to control load movement — never guide loads by hand
Learn standard hand signals; use a qualified signal person
NEVER stand under a suspended load — the #1 rigging safety rule
Inspect all rigging equipment before each shift

## Slide 6
QUIZ / DISCUSSION
1
What is the capacity factor of a sling used at a 45-degree angle?
Answer: 71% of the sling's rated capacity. A sling rated at 10,000 lbs can only safely lift 7,100 lbs at a 45° angle.
2
Name two conditions that require a wire rope sling to be removed from service.
Answer: Any two of: six or more broken wires in one lay, kinking, crushing, bird-caging, corrosion, heat damage, or a missing/unreadable capacity tag.
3
What is the single most important rule in rigging safety?
Answer: Never stand under a suspended load. If the rigging fails or the load shifts, anyone underneath is at risk of fatal injury.

## Slide 7
ATTENDANCE SIGN-OFF
Rigging Safety Fundamentals
# | Print Name | Signature | Company | Date
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
By signing above, I confirm that I attended this toolbox talk and understand the material presented.