## Slide 1
LOCKOUT/TAGOUT (LOTO)
29 CFR 1910.147
Presenter: ____________________ Date: ____________________
FORBES SAFETY SOLUTIONS
TOOLBOX TALK

## Slide 2
WHY THIS MATTERS
Failure to control hazardous energy kills an estimated 48 workers per year and causes 17,690 lost-workday injuries (NSC 2023 data).
OSHA estimates that proper compliance with the LOTO standard would prevent 120 fatalities and 50,000 injuries every year.
LOTO violations are consistently in OSHA's Top 10 most cited standards. "I thought the power was off" has been the last thought of too many workers.
Hazardous energy doesn't just mean electrical. Hydraulic lines hold pressure, springs store mechanical energy, pipes carry steam, and chemical reactions continue after shutdown.
Every incident investigation involving uncontrolled energy comes back to the same root cause: someone skipped a step because they were in a hurry.
Source: OSHA LOTO Fact Sheet
FORBES SAFETY SOLUTIONS

## Slide 3
ENERGY TYPES & ISOLATION PROCEDURES
Six energy types to control: ELECTRICAL (disconnect and verify zero energy), MECHANICAL (block/secure moving parts), HYDRAULIC (bleed lines and block), PNEUMATIC (bleed air pressure), THERMAL (allow cool-down or insulate), CHEMICAL (drain, purge, or neutralize).
Every piece of equipment must have a written, machine-specific LOTO procedure. Generic procedures get people killed — each machine has unique energy sources and isolation points.
The isolation sequence: (1) Notify all affected employees, (2) Shut down equipment using normal stopping procedure, (3) Isolate ALL energy sources, (4) Apply YOUR lock and tag, (5) Verify zero energy state.
Verification is the most skipped and most critical step. After lockout, attempt to start the equipment. Test circuits with a meter. Bleed trapped pressure. Verify. Every. Time.
Tags are NOT locks. A tag is a warning device only — it does not physically prevent operation. Every worker in the danger zone must apply their own lock.
Source: OSHA 29 CFR 1910.147
FORBES SAFETY SOLUTIONS

## Slide 4
GROUP LOTO & CRITICAL RULES
Group LOTO: When multiple crews work on the same equipment, a primary authorized employee coordinates lockout. Each worker still applies their own lock to a group lockbox.
Shift change protocol: The outgoing shift cannot remove their locks until the incoming shift has applied theirs. There must be zero gap in protection.
NEVER remove another person's lock. The only person who removes a lock is the person who put it on. If they left site, follow the employer's specific lock-removal procedure with supervisor authorization and documented verification.
Try-out procedure after maintenance: Ensure all workers are clear, all tools removed, guards replaced, then remove locks in reverse order. The primary authorized employee removes the last lock.
Annual inspections of LOTO procedures are required. An authorized employee who does NOT normally use the procedure must review it. Document the review with names, dates, and equipment covered.
Source: OSHA 29 CFR 1910.147
FORBES SAFETY SOLUTIONS

## Slide 5
DISCUSSION QUESTIONS
Take 5 minutes to discuss with your crew:
1. Can you name all the energy sources on the equipment you're working with today? Are you sure you've got them all?
2. When was the last time you actually tried to start a machine after locking it out to verify zero energy?
3. Have you ever been pressured to skip LOTO because the job would "only take a minute"? What happened?
4. If you found a lock on equipment with no tag or an unreadable tag, what would you do?
FORBES SAFETY SOLUTIONS

## Slide 6
ATTENDANCE SIGN-OFF
Date: ____________ Topic: Lockout/Tagout (LOTO) Presenter: ____________________
# | PRINT NAME | COMPANY | SIGNATURE
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  | 
FORBES SAFETY SOLUTIONS