## Slide 1
FORBES SAFETY SOLUTIONS
ELECTRICAL SAFETY
& ARC FLASH AWARENESS
Toolbox Talk — Electrical Hazard Awareness
[Company Name]
[Date]
Reference: 29 CFR 1910.331-335 | NFPA 70E | 29 CFR 1926.405

## Slide 2
WHY THIS MATTERS
Arc flash can reach temperatures of 35,000°F — four times hotter than the surface of the sun.
~1,000
Electrical injuries
per year in
U.S. workplaces
5–10
Arc flash incidents
per day in the U.S.
(NFPA data)
35,000°F
Arc flash
temperature —
explosive force
Source: NFPA 70E, BLS Electrical Injuries

## Slide 3
ARC FLASH & APPROACH BOUNDARIES
WHAT IS ARC FLASH?
An arc flash is an explosive release of energy caused by an electrical fault between conductors or a conductor and ground.
Dangers include:
Temperatures up to 35,000°F
Explosive pressure wave (blast)
Molten metal shrapnel
Intense light — can cause blindness
Severe burns and hearing damage
APPROACH BOUNDARIES (NFPA 70E)
BOUNDARY | WHO MAY ENTER | REQUIREMENT
Arc Flash Boundary | Qualified / Unqualified w/ PPE | Arc-rated PPE required
Limited Approach | Qualified persons only | Shock hazard awareness
Restricted Approach | Qualified with written plan | Insulated tools & shock PPE
Prohibited Approach | Same as direct contact | Same PPE as direct contact

## Slide 4
PPE CATEGORIES & QUALIFIED PERSONS
ARC FLASH PPE CATEGORIES (NFPA 70E)
CAT | cal/cm² | REQUIRED PPE
1 | 4 | Arc-rated shirt/pants, safety glasses, hearing protection, leather gloves
2 | 8 | Cat 1 + arc-rated face shield, balaclava
3 | 25 | Arc flash suit hood, arc-rated jacket/pants, insulated gloves w/ leather protectors
4 | 40 | Multi-layer arc flash suit, heavy-duty insulated gloves, full face shield + hood
QUALIFIED VS. UNQUALIFIED
Qualified Person:
Trained to work on or near exposed energized parts
Can identify hazards and determine approach boundaries
Authorized to enter restricted/prohibited boundaries
Unqualified Person:
Must stay outside the limited approach boundary
May NOT work on energized equipment
Must be escorted if entering limited boundary

## Slide 5
KEY ELECTRICAL SAFETY RULES
DE-ENERGIZE FIRST
De-energizing is ALWAYS the safest option.
Lockout/Tagout (LOTO) Steps:
Notify all affected employees
Identify all energy sources
Isolate energy sources
Apply lockout/tagout devices
Verify zero energy state
Test before you touch!
CONSTRUCTION SITE REQUIREMENTS
GFCIs required on all construction sites
(29 CFR 1926.405)
Inspect all cords and tools before each use
Keep minimum 10 ft clearance from overhead power lines (up to 50kV)
Never use damaged cords — replace immediately
Do not overload circuits or use multi-outlet adapters
Mark all electrical panels — keep 36" clearance
Report any shock, tingle, or sparking immediately

## Slide 6
QUIZ / DISCUSSION
Q1
What is the safest approach before performing electrical work?
Answer: De-energize the equipment first using Lockout/Tagout (LOTO) procedures, then verify zero energy before starting work.
Q2
What PPE category requires a full arc flash suit, and what is its cal/cm² rating?
Answer: Category 4 — rated at 40 cal/cm². Requires multi-layer arc flash suit, heavy-duty insulated gloves, full face shield and hood.
Q3
Can an unqualified person work inside the limited approach boundary?
Answer: No. Unqualified persons must stay outside the limited approach boundary and may only enter if escorted by a qualified person.

## Slide 7
ATTENDANCE SIGN-OFF
By signing below, I acknowledge that I attended and understood this Toolbox Talk on Electrical Safety / Arc Flash Awareness.
# | PRINTED NAME | SIGNATURE | DATE
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  |