## Slide 1
TRENCHING & EXCAVATION SAFETY
29 CFR 1926.650-652
Presenter: ____________________ Date: ____________________
FORBES SAFETY SOLUTIONS
TOOLBOX TALK

## Slide 2
WHY THIS MATTERS
Trench collapses killed 39 workers in 2022 — the worst year in a decade. Numbers dropped to 15 in 2023 and 12 in 2024 after OSHA's zero-tolerance enforcement push.
One cubic yard of soil weighs as much as a car — roughly 3,000 lbs. A partial collapse can pin you in seconds and crush your chest so you can't breathe.
85% of all trenching fatalities from 2011-2021 occurred in the construction industry (CPWR/BLS data).
OSHA has a zero-tolerance policy for unprotected trenches: immediate inspections, willful citations, and criminal prosecution referrals.
The average rescue time for a buried worker is 6+ minutes. The survival window for full burial is about 4 minutes. You have to get it right before anyone goes in.
Source: OSHA Trench Safety Data
FORBES SAFETY SOLUTIONS

## Slide 3
COMPETENT PERSON & SOIL CLASSIFICATION
A Competent Person must be on site at all times when workers are in the trench. This person has the authority to shut down work immediately — no foreman override.
The Competent Person classifies soil before any worker enters: Type A (most stable, e.g. clay), Type B (medium, e.g. crusite gravel), Type C (least stable, e.g. wet sand). When in doubt, assume Type C.
Soil classification determines your protective system: Type A can use 3/4:1 slopes, Type B needs 1:1, Type C needs 1.5:1 — or use shoring/shielding.
Previously disturbed soil is NEVER Type A, regardless of what it looks like. If a trench was backfilled and re-dug, default to Type B at best.
Daily inspections are required before each shift, after rain, and after any event that could change conditions. Document everything.
Source: OSHA 29 CFR 1926.652
FORBES SAFETY SOLUTIONS

## Slide 4
PROTECTIVE SYSTEMS & ACCESS/EGRESS
Three protective system options: SLOPING (cutting walls back at safe angles), SHORING (hydraulic or timber supports), or SHIELDING (trench boxes). Choose based on soil type, depth, and site conditions.
Any trench 5 feet or deeper requires a protective system unless the Competent Person determines the excavation is in stable rock. No exceptions.
Trenches 4 feet or deeper require a ladder, ramp, or stairway within 25 feet of every worker. You should never have to walk more than 25 feet to get out.
Never stack spoil piles, equipment, or materials within 2 feet of the trench edge. That weight can trigger a collapse.
Water accumulation is a collapse trigger. Pump standing water before entry and monitor continuously. Rain overnight? Re-inspect before anyone goes in.
Source: OSHA Trenching & Excavation
FORBES SAFETY SOLUTIONS

## Slide 5
DISCUSSION QUESTIONS
Take 5 minutes to discuss with your crew:
1. Who is the Competent Person on this site today? Does every crew member know who that is?
2. What soil type are we working in right now — and how was that classification made?
3. How far is the nearest exit point from where workers are in the trench? Is it within 25 feet?
4. If a wall started to crack or bulge right now, what's your immediate response?
FORBES SAFETY SOLUTIONS

## Slide 6
ATTENDANCE SIGN-OFF
Date: ____________ Topic: Trenching & Excavation Safety Presenter: ____________________
# | PRINT NAME | COMPANY | SIGNATURE
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  | 
FORBES SAFETY SOLUTIONS