## Slide 1
FALL PROTECTION
29 CFR 1926.501-503
Presenter: ____________________ Date: ____________________
FORBES SAFETY SOLUTIONS
TOOLBOX TALK

## Slide 2
WHY THIS MATTERS
Falls are the #1 killer in construction. In 2024, falls to a lower level caused 370 fatalities among construction and extraction workers — over a third of all construction deaths (BLS CFOI 2024).
Fall Protection has been OSHA's most cited violation for 15 consecutive years, with over 7,000 citations issued in FY 2024 alone.
The average fall fatality happens from just 6 to 10 feet. You don't need to be on a high-rise to die.
Most fall deaths are 100% preventable. The equipment exists. The standards are clear. The gap is compliance.
A single fall fatality can result in OSHA penalties exceeding $150,000, criminal referrals, and project shutdowns.
Source: OSHA Fall Prevention Campaign
FORBES SAFETY SOLUTIONS

## Slide 3
100% TIE-OFF & ANCHORAGE POINTS
100% tie-off means you are connected at ALL times when at 6 feet or above — no exceptions for "just a second" or "I'm almost done."
Anchorage points must support 5,000 lbs per worker or be designed by a qualified person as part of a complete PFAS with a safety factor of 2.
Never tie off to conduit, vents, antenna mounts, or anything you haven't verified. If you wouldn't hang your truck from it, don't hang yourself from it.
When moving between anchorage points, use a dual-lanyard system so one hook is always connected before the other releases.
Guardrails are the first line of defense — they protect without any action from the worker. Use them wherever feasible before defaulting to personal fall arrest.
Source: OSHA 29 CFR 1926.502
FORBES SAFETY SOLUTIONS

## Slide 4
HARNESS INSPECTION & RESCUE PLANNING
Inspect harnesses before every use with the ABC method: A = Anchors/D-rings (centered between shoulder blades), B = Buckles/Belts (no fraying, all buckles lock), C = Connections/Straps (no cuts, burns, chemical damage).
Any harness involved in a fall arrest event must be immediately removed from service and destroyed — no exceptions, even if it "looks fine."
Rescue planning is not optional. OSHA requires a rescue plan BEFORE anyone goes to height. "Call 911" is not a rescue plan — suspension trauma can kill in under 30 minutes.
Every crew working at height must have a rescue method available: self-rescue training, rescue team on standby, or mechanical retrieval equipment.
Never modify, paint, or attach unauthorized items to fall protection equipment. If the manufacturer didn't put it there, it doesn't belong.
Source: OSHA 29 CFR 1926.503
FORBES SAFETY SOLUTIONS

## Slide 5
DISCUSSION QUESTIONS
Take 5 minutes to discuss with your crew:
1. Where on this jobsite are we most exposed to fall hazards today? Are all those areas controlled?
2. When was the last time you actually inspected your harness — and what would you look for?
3. If someone on your crew went into suspension right now, what's our plan to get them down in under 6 minutes?
4. Have you ever seen someone skip their tie-off "just for a second"? What would you say to them?
FORBES SAFETY SOLUTIONS

## Slide 6
ATTENDANCE SIGN-OFF
Date: ____________ Topic: Fall Protection Presenter: ____________________
# | PRINT NAME | COMPANY | SIGNATURE
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  | 
FORBES SAFETY SOLUTIONS