## Slide 1
Personal Fall Arrest System
(PFAS) Inspection
Pre-Use Inspection Requirements for Harnesses, Lanyards & SRLs
Ref: 29 CFR 1926.502(d), ANSI Z359.11
Forbes Safety Solutions

## Slide 2
Why PFAS Inspection Matters
395
Fatal falls in construction in a recent year — many involving failed or uninspected fall protection
100%
PFAS must be inspected before EVERY use — no exceptions
1 Fall
After a single fall arrest event, the entire PFAS must be removed from service permanently

## Slide 3
Inspecting Your Harness
Check all webbing for cuts, frays, burns, chemical damage, abrasion, and pulled stitching — run the webbing through your hands inch by inch
Inspect D-rings (dorsal, sternal, side): look for cracks, distortion, corrosion, sharp edges, and proper movement
Examine all buckles: ensure they lock and release properly, check for deformation, corrosion, and missing components
Verify labels are legible: manufacturer, model, date of manufacture, and standards compliance (ANSI Z359.11) must be readable
Check grommets and hardware attachment points for looseness, corrosion, or damage
Inspect all stitching — especially load-bearing bar-tack stitching — for broken threads, pulled seams, or UV degradation
Ref: 29 CFR 1926.502(d), ANSI Z359.11

## Slide 4
Inspecting Lanyards & Self-Retracting Lifelines
Lanyards: check webbing or cable for cuts, kinks, frays, burns, abrasion, and corrosion along the entire length
Snap hooks: verify the gate locks properly, the keeper spring returns fully, and there is no corrosion or distortion
Shock absorber pack: inspect the outer cover for tears or deployment indicators — if the pack shows signs of activation, remove from service
Self-Retracting Lifelines (SRLs): extend and retract the line fully — it should retract smoothly without sticking or jerking
Check the SRL housing for cracks, dents, and corrosion — inspect the mounting bracket and swivel for damage
Verify the SRL label: check manufacture date, inspection date, and that annual competent-person inspection is current
Ref: 29 CFR 1926.502(d), ANSI Z359.11

## Slide 5
Removal from Service, Storage & Documentation
Remove from service IMMEDIATELY after any fall arrest event — the harness, lanyard, and all connectors must be destroyed or returned to manufacturer
Remove from service if you find any visible damage: cuts, frays, deformation, corrosion, label illegibility, or broken stitching
Remove expired equipment per manufacturer guidelines — do not exceed the recommended service life
Store PFAS in a clean, dry, cool area away from chemicals, UV light, moisture, and sharp objects
Never hang equipment on nails or sharp hooks — use wide hangers or storage bags
Document every inspection: date, inspector name, equipment serial number, condition, and pass/fail determination
Ref: 29 CFR 1926.502(d), ANSI Z359.11

## Slide 6
Knowledge Check
Q1: How often must a personal fall arrest system be inspected?
A: Before every use — a pre-use inspection is required each time the equipment is put on.
Q2: What must happen to a harness and lanyard after they arrest a fall?
A: They must be immediately removed from service — the entire system must be destroyed or returned to the manufacturer.
Q3: Name three things to check when inspecting a harness.
A: Webbing for cuts/frays, D-rings for cracks/distortion, and buckles for proper locking — plus legible labels and intact stitching.

## Slide 7
PFAS Inspection — Sign-Off Sheet
By signing below, I confirm I attended this Toolbox Talk and understand the material presented.
# | Print Name | Signature | Date
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  |