## Slide 1
FORBES SAFETY SOLUTIONS
Fire Prevention on the Jobsite
Ref: 29 CFR 1926.150–155 — Fire Protection and Prevention
[Company Name]
[Date]
TOOLBOX TALK

## Slide 2
WHY THIS MATTERS
4,000+
Structure fires at construction sites reported annually in the United States
$300M+
Annual property damage from fires on construction and renovation sites
37%
Of construction fires are caused by hot work operations (cutting, welding, brazing)

## Slide 3
Common Fire Causes on Construction Sites
IGNITION SOURCES
Hot work: welding, cutting, brazing, soldering — sparks can travel 35+ feet
Electrical faults: overloaded circuits, damaged cords, temporary wiring
Temporary heating devices placed too close to combustibles
Smoking in unauthorized areas
Improperly discarded rags soaked with solvents or oils
FUEL SOURCES & CONDITIONS
Flammable liquids: gasoline, solvents, adhesives, paints stored improperly
Combustible construction materials: lumber, insulation, packaging
Accumulated trash, sawdust, and debris on site
Compressed gas cylinders stored near heat sources
Poor housekeeping is the #1 contributing factor to fire spread

## Slide 4
Fire Extinguisher Use & Response
P.A.S.S. TECHNIQUE
P — PULL the pin to unlock the extinguisher
A — AIM the nozzle at the base of the fire, not the flames
S — SQUEEZE the handle to release the extinguishing agent
S — SWEEP side to side at the base until the fire is out
Stand 6–8 feet from the fire; back away facing the fire area
FIGHT OR EVACUATE?
ONLY fight a fire if: it is small (trash can size), you have a clear escape route, the extinguisher is rated for the fire type, and you are trained
EVACUATE if: fire is spreading, room fills with smoke, you are unsure, or extinguisher is empty/ineffective
Always alert others and call 911 before attempting to fight
Know your site evacuation routes and assembly points

## Slide 5
Hot Work Permit & Housekeeping Requirements
Requirement | Standard | Key Details
Hot Work Permit | Required | Written permit for all welding, cutting, brazing operations
Fire Watch | 30 min minimum | Trained person monitors area during and 30 min after hot work
Extinguisher distance | Within 25 ft | Fully charged, correct type extinguisher within travel distance
Flammable storage | Approved cabinets | Max 25 gallons per cabinet; away from ignition sources
Combustible clearance | 35 ft radius | Remove or cover combustibles within 35 ft of hot work
Daily cleanup | End of shift | Remove trash, oily rags, and debris daily; rags in metal containers with lids

## Slide 6
QUIZ / DISCUSSION
1
What does P.A.S.S. stand for when using a fire extinguisher?
Answer: Pull the pin, Aim at the base of the fire, Squeeze the handle, Sweep side to side.
2
How long must a fire watch be maintained after hot work is completed?
Answer: A minimum of 30 minutes after hot work operations have ended to ensure no smoldering material remains.
3
Name two conditions where you should evacuate rather than fight a fire.
Answer: Any two of: the fire is spreading rapidly, the room is filling with smoke, you don't have a clear escape route, the extinguisher is empty or ineffective, or you are untrained.

## Slide 7
ATTENDANCE SIGN-OFF
Fire Prevention on the Jobsite
# | Print Name | Signature | Company | Date
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
By signing above, I confirm that I attended this toolbox talk and understand the material presented.