## Slide 1
HEAT ILLNESS PREVENTION
OSHA Heat NEP & State Standards (CA, TX, AZ, NM)
Presenter: ____________________ Date: ____________________
FORBES SAFETY SOLUTIONS
TOOLBOX TALK

## Slide 2
WHY THIS MATTERS
Heat killed at least 211 workers between 2017 and 2022, and those numbers significantly undercount the true toll — many heat deaths are recorded as heart attacks or falls (EPI/BLS data).
An estimated 28,000 workplace injuries per year are directly linked to working on hot days, affecting virtually every industry including indoor work (GW/Harvard 2025 study).
Injury risk starts climbing at a heat index of 85°F and rises steeply above 90°F. By the time it "feels hot," you're already in the danger zone.
New and returning workers are at the highest risk. Over 50% of heat-related deaths occur in a worker's first few days on the job.
States like California, Arizona, Texas, and New Mexico have specific heat regulations. Know your state's trigger temperatures and required rest breaks.
Source: Economic Policy Institute - Extreme Heat
FORBES SAFETY SOLUTIONS

## Slide 3
HEAT STROKE vs. HEAT EXHAUSTION
HEAT EXHAUSTION: Heavy sweating, cold/clammy skin, weak pulse, nausea, dizziness, headache. The body is still trying to cool down. Move to shade, cool water, loosen clothing.
HEAT STROKE: Body temp above 103°F, hot/red/DRY skin (sweating has stopped), rapid strong pulse, confusion, slurred speech, loss of consciousness. THIS IS A MEDICAL EMERGENCY — call 911 immediately.
The critical difference: heat exhaustion is the warning, heat stroke is the failure. If you miss the warning, you're fighting for someone's life.
Water-Rest-Shade is the rule. Drink water every 15-20 minutes even if you don't feel thirsty. By the time you're thirsty, you're already behind on hydration.
Acclimatization protocol: New workers or those returning from 7+ days off must ramp up over 14 days — start at 20% workload on day 1 and increase by no more than 20% per day.
Source: OSHA Heat Illness Prevention
FORBES SAFETY SOLUTIONS

## Slide 4
FIELD PROCEDURES & EMERGENCY RESPONSE
Buddy system is mandatory in high-heat conditions. Never let someone work alone — confused workers don't recognize their own symptoms.
Pre-shift planning: Check the heat index forecast. Above 80°F, increase water and shade. Above 90°F, implement mandatory rest cycles. Above 105°F, consider rescheduling work.
Provide cool (not ice cold) drinking water at the rate of 1 quart per hour per worker, positioned within easy walking distance. No water = no work.
Shade or air-conditioned rest areas must be available when temps exceed trigger levels. Workers showing ANY symptoms must be relieved immediately — do not wait for them to ask.
Emergency action: If someone shows heat stroke signs (confusion, no sweating, hot skin), call 911 immediately, move them to shade, apply cold water/ice to neck, armpits, and groin. Do not give fluids if unconscious.
Source: OSHA Heat NEP
FORBES SAFETY SOLUTIONS

## Slide 5
DISCUSSION QUESTIONS
Take 5 minutes to discuss with your crew:
1. How much water have you actually drunk today? Could you point to where the nearest water and shade station is right now?
2. Do we have any new workers on the crew this week? Are they on an acclimatization schedule?
3. What's the difference between heat exhaustion and heat stroke — and what do you do for each?
4. Who is your buddy today? Would you know if they were starting to show symptoms?
FORBES SAFETY SOLUTIONS

## Slide 6
ATTENDANCE SIGN-OFF
Date: ____________ Topic: Heat Illness Prevention Presenter: ____________________
# | PRINT NAME | COMPANY | SIGNATURE
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  | 
FORBES SAFETY SOLUTIONS